## Slide 1
Team-based Integrated Circuit Design
ECE 482
Alec Wasowicz

## Slide 2
Working as a Team

## Slide 3
Real world IC design is far too complex for a single person
Efficient work relies on two processes
  Assigned job roles
    Layout Engineer
    Design Engineer
    Test Engineer
  Modular, hierarchy-based design
    Independent, functional blocks are created separately and then merged to finish the final design
Introduction Slides
In this class, we want all students to understand the full process of IC design. Therefore, it is NOT recommended to follow this strategy just yet.

## Slide 4
There is no “correct” way to set up a team
Every good way shares some habits
  Clear communication about design decisions, practices, and naming conventions
  Contribution from every group member
This presentation is designed to give a rough overview of how IC design as a team works, not an exact guide
Introduction Slides

## Slide 5
Hierarchy-based Design

## Slide 6
Designs are broken down into functional blocks
  Simplify schematic and layout for understanding
  Breaks the work into manageable pieces
  Allows copies of similar circuits to save time
Each block is independent except for the pre-determined interactions with other blocks
  I.e. The logic designer doesn’t care how the clock is generated, just that it will be provided to their functional block
  The design of each block is decoupled from how the other functions are realized in circuitry
Hierarchy

## Slide 7
Hierarchy Example
Simple Microcontroller
Logic
Clock Generation
External IO
Memory
SRAM
Addressing
Next State
Output
Divider
Buffers
Receiver
Transmitter
Top Cell
Functional Block
Sub Cell
Simple Logic Gates (NAND, NOR, INV, etc.)
Logic Gates
Device Level (PMOS, NMOS, Diode, Resistor, Capacitor, etc.)
Transistors
On a 4-person team, each engineer might design 1 functional block.

## Slide 8
Version Control

## Slide 9
We just showed how hierarchy breaks down a large design into manageable chunks
  However, this has turned 1 large design file into many small files
This introduces some concerning questions:
  How do I know I have the correct version of a cell?
  Did my teammate make a change to their block?
  What if I accidentally delete/break my teammate’s block?
The problems with hierarchy

## Slide 10
We clear up these questions by being organized
  Declare a functional version of the project as the main version in a central repository
    Doubles as backup in case of errors
  When you want to update a file, edit a local copy of the main version
    For clarity, only have 1 person editing a specific file at a time
  When finished, insert the file into the reference version
    Let your team know the file is done being updated
The solution: Version Control

## Slide 11
In Industry, it’s common practice to have a Design Management software that takes care of version control for us
  We simply “check-out” a file for editing, locking the file to read-only for everyone else
  When done, we “check-in” the file and it becomes the current, working version
Unfortunately, software-based version control isn’t possible in EWS
Version Control in Industry

## Slide 12
You can practice version control using Google Drive and a word document
  Store copies of your project in a shared folder
  Manually track changes in the word document
Work-around: Pseudo Design Management

## Slide 13
“ece482_project” is the library I created in Cadence
  A directory with the same name is created in ece482.work
  Each cell is stored as its own folder within this directory
  To update the reference design, I upload my version to Drive
  To update my version, I download and replace the folder in my EWS workspace
    Do this with Cadence closed
What this looks like in Linux

## Slide 14
topcell schematic instantiates symbols of the lower level blocks instead of circuit elements
  Look at Cadence documentation if you don’t know how to make/instantiate a symbol
topcell layout uses lower level layouts in a similar way
What the design looks like
Schematic for “topcell”

## Slide 15
Don’t update the team’s shared repository until your local version is functional after your edits
Communicate with your team
  Be clear on what’s expected from each block, naming conventions, layout conventions
  The more in-sync you are, the more productive your team can be
These have been rough guidelines. Many companies implement these systems slightly differently
  If your team finds a much more efficient method, feel free to use it
  (And share it on Piazza, not every student starts 482 with Cadence experience)
Final Reminders